## Slide 1: EEG MVPA scripts 1.0
Johannes Fahrenfort

## Slide 2: What we’ll cover
Analysis
Visualization and statistics
Just very briefly:
How this works with Lisa computing grid

## Slide 3: scripts
Not yet on Github (but this is on my to do list)
Freely available, I can give you non-write dropbox shared access
If you need support, I am willing and able
For considerable help at any phase, co-authorship would be much appreciated

## Slide 4: Workflow
Preprocessing
MVPA analysis
Visualization
Group stats
Local machine
Lisa cluster
Preprocessing
MVPA analysis
No GUI

## Slide 5: Pre-processing
Up to you, as long as the data are EEGlab format (.set files)
I have found that removing eye-blinks has very little (=no) impact on classification accuracy, but my tasks have occipital sources of course
My personal pipeline:
  Resample to 512 Hz (if applicable)
  Highpass filter (.1 Hz)
  Remove muscle artifact using customized fieldtrip script
  Epoch data, use numbers for conditions

## Slide 6: Organization of scripts
scripts
run_pre_processing.m
run_RAW_eeglab_decoding.m
run_TFR_decoding.m
run_plotting_EEG.m
matlab_scripts
behavior
eeg_preprocessing
eeg_mvpa
… etc
Experiment- specific scripts
Always local
Core library functions
Local and on server
I will give examples of these during this presentation

## Slide 7: MVPA analysis
Functionality - two core functions:
  classify_RAW_eeglab_data.m
  classify_TFR_data_from_eeglab.m
  Always the same structure:
  function(filepath,filenames,outpath,<varargs>)

## Slide 8: classify_RAW_eeglab_data.m
Performs MVPA analysis on eeglab data
Assume we want to perform analysis on one subject, running locally inside matlab:

## Slide 9: /Users/VU-MBP/data

## Slide 10: settings
nFolds = how many folds you want to use in k-fold leave-one-out procedure
cChannelset = predefined channelsets to select electrodes (1 = uses all electrodes; 2 = uses occipital electrodes, 3 = uses parietal electrodes etc.), or like this 'Oz,Pz,Iz’
method = the method the LDA uses (e.g. linear), see and other options (e.g. hr-far, bin, bintrain, bintest, randperm), see

## Slide 11: settings
crossclass = compute only along the diagonal or compute the Generalization Across Time (GAT) matrix. This takes a LOT of time. You can add a second value to downsample the signal, like this: e.g. to downsample to 128 Hz (faster).
erp_baseline = baseline that should be used for each trial, e.g. uses a baseline between -250 and 0 ms.

## Slide 12: settings
conditions: indicate the condition classes you want to do classification for, should be string!
Very useful function: cond_string.m

## Slide 13: example in output folder (20 subjects)
the channel set that was used

## Slide 14: example output in matlab (1 subject)

## Slide 15: settings

## Slide 16: Confusion matrix
A confusion matrix is a table that is used to describe the performance of a classification model (or "classifier") on a set of test data for which the true values are known.

## Slide 17: LabelsOverTime
Confusion matrix: folds * time (test) * time (train) * stimclass (actual) * stimclass (classifier)

## Slide 18: ClassOverTime
Example average accuracy performance:
n= 60
n= 105
Perf = 50/60 = .83
Perf = 100/105 = .95
Average performance = (.83 + .95)/2 = .89
(so NOT 150/165 = .91!)

## Slide 19: ClassOverTime
You can also compute hr-far, d’ and other SDT measures (see help). This can only be done when you have only signal and noise. To do this, specify: or When you do this, the first label should always be the signal, and the second label the noise stimulus!

## Slide 20: ClassOverTime

## Slide 21: classify_TFR_data_from_eeglab.m
The same principle, but now for time frequency
This is a wrapper function which internally uses classify_TFR_data.m and compute_TFR_from_eeglab.m
For help on MVPA settings do:
For TFR settings do (and/or modify):

## Slide 22: classify_TFR_data_from_eeglab.m
Running locally inside matlab:
Other options are:
‘evoked’ and
‘induced’ power

## Slide 23: TFR settings
resample_to = New sampling rate for the TFR analysis. Since the TFR signal is already intrinsically temporally smoothed, you don’t require all time samples.
TFRmethod: total, evoked or induced, do you want total, evoked or induced TFRs. bin: do you want to take the average of the condition labels in each condition.
Frequencies: can run up to 100, take frequency steps of 2.

## Slide 24: example in output folder (20 subjects)
time * time, separately for each frequency
frequency * time, all frequencies

## Slide 25: example output (1 subject)

## Slide 26: settings

## Slide 27: settings
cond1
cond2
cond3
cond4
cond5
cond6

## Slide 28: ClassOverTime

## Slide 29: Things to note
You can also indicate that you want to use a different dataset for training and for testing
For example like this:
training file testing file
training labels testing labels

## Slide 30: Group statistics and plotting
Statistics
RAW:
  2D (only diagonal)
  3D (Generalization Across Time: GAT)
TFR:
  3D (frequency-time)
  3D (GAT, for a specific frequency)

## Slide 31: Three core functions
Functionality: computing group averages + stats and plotting the classification results + topomaps
compute_group_MVPA.m
plot_MVPA.m
plot_MVPA_weights.m
First run compute_group_MVPA, then plot the result using plot_MVPA

## Slide 32: compute_group_MVPA.m
cluster_based, see: Maris, E., & Oostenveld, R. (2007). Nonparametric statistical testing of EEG- and MEG-data. Journal of Neuroscience Methods, 164(1), 177–190. http://doi.org/10.1016/J.Jneumeth.2007.03.024
fdr, see: Benjamini, Y., & Hochberg, Y. (1995). Controlling the False Discovery Rate - a practical and powerful approach to multiple testing. Journal of the Royal Statistical Society Series B-Methodological, 57(1), 289–300.

## Slide 33: output of compute_group_MVPA.m
stats
weights
gsettings

## Slide 34: stats

## Slide 35: weights
CovPatterns and CorPatterns are the product of weight matrix and data covariance and correlation matrix respectively. They are interpretable as neural sources, see
Haufe, S., Meinecke, F., Goergen, K., Daehne, S., Haynes, J.-D., Blankertz, B., & Biessgmann, F. (2014). On the interpretation of weight vectors of linear models in multivariate neuroimaging. NeuroImage, 87, 96–110. http://doi.org/10.1016/j.neuroimage.2013.10.067

## Slide 36: gsettings
What you specified 4 slides back

## Slide 37: plot_MVPA.m
Add on to gsettings

## Slide 38: 2D plot

## Slide 39: 3D (GAT)

## Slide 40: 3D (time-frequency)

## Slide 41: 2D (frequency = 10)

## Slide 42: 3D (GAT, frequency 10 Hz)

## Slide 43: Other stuff:
Extract values from your matrices: mask is a matrix that has the same size as stats.ClassOverTime, containing 1’s for regions that should be extracted and 0’s elsewhere. It outputs averages(cRoi,cCond,cSubj)

## Slide 44: Weight and source topoplots
Only works properly when you include all electrodes in the MVPA analysis of course
Only makes sense when you plot the relation between two stimulus classes (scripts currently also only work when the initial analysis had two stimulus classes)

## Slide 45: Weight and source topoplots
correlation/class separability map

## Slide 46: weights (left) and correlation/class separability map(right)
Of course you can also plot based on covariance matrix, see Haufe (2014) for details

## Slide 47: So what about automation, Lisa etc?
Preprocessing
MVPA analysis
Visualization
Group stats
Local machine
Lisa cluster
Preprocessing
MVPA analysis

## Slide 48: Running jobs on Lisa
Functionality - two core functions:
create_qsub_files.m
run_local_instead_of_qsub.m
Always the same structure: create_qsub_files(path_to_function, function_name, qsettings, <varargs belonging to function: filepath,filenames,outpath, varargs etc>)

## Slide 49: create_qsub_files.m
Allows you to run all your subjects and all your parameter combinations in a single command
Very powerful, but requires a bit of setup
Creates job on Lisa computing cluster, which can be submitted and then creates all the output at once
Will discuss this in detail another time, first process all of this, if some of you are interested, I will set up a second meeting to go over this